Communal Dry Pit Latrine (4 seats) including 1 room for shower

Summary of Work

# Sub Structure

1. Excavation and earthwork ------------------------------------------------ 1,635.00 Birr

2. Masonry work -------------------------------------------------------------- 4,420.00 Birr

3. Concert Work  -------------------------------------------------------------- 6,394.00 Birr

# Super Structure

4.  Concert Work  ------------------------------------------------------------- 2,696.14Birr

5. Walling	---  ----------------------------------------------------------------- 4,420.00 Birr

6. Roofing  --------------------------------------------------------------------- 2,210.00 Birr

7. Door-------------------------------------------------------------------------- 2,800.00 Birr

8. Finishing Work   ---------------------------------------------------------- 3,520.00 Birr

## Total ---------------------------------------------------------------------------  28,095.14 Birr

Contingency 10% ---------------------------------------------------    2,809.51 Birr

Grand Total ---------------------------------------- 30,904.65 Birr

| No. | Description | Unit of Measurement | Quantity | Unit price (in Birr) | Total |
| --- | --- | --- | --- | --- | --- |
| 1.1. 1.2. 1.3. 1.4. 2.1. 3.1. 3.2. 3.3. . 4.1. 4.2. 4.3 . 5.1 5.2 6.1. 7.1. 8.1. 8.2. | A. Super Structure 1. Excavation and Earth Work Clear the site at the depth of 10 cm. Excavate for dry pit latrine in ordinary soil to a depth not exceeding 300 cm. Below ground Cart away surplus excavated materials from the site and dispose off at a distance directed by the engineer Fill Suitable soil from the site around foundation wall well compacted in a layer not exceeding 25 cm. thick Total carried to summary 2. Masonry Work At bottom 80 cm. And at top 50 cm. Thick stone masonry lining for pit latrine vertically dry jointed and horizontally joints are to be mortared in co firmly with line and grades shown on the drawing Total carried to summary 3. Concert Work Reinforced concert class C-25 or 360Kg. Cement/ M3 perm filled into formwork and vibrated around rod reinforcement steel and formwork measure separated a. In grade beam b. In 10 cm. Thick floor slab Provide, cut and fix sawn Zigba wood formwork price includes scaffolding and other necessary materials a. In grade beam Steel reinforcement according to structural drawing price includes bending, cutting, placing and tying with wires a. 6 mm. Plain bar b. 8 mm. Deformed bar. 14 mm. Deformed bar 16 mm. Deformed bar Total Carried to summary B. Super Structure 4. Concert Work Concert work as described before. Steel reinforcement and formwork measured separately. All Exposed concert shall be hammered and plastered. in elevation column in top tie beam Provide, cut and fix sawn Zigba wood formwork price includes scaffolding and other necessary materials in elevation column in top tie beam Steel reinforcement according to structural drawing price includes bending, cutting, placing and tying with wires a. 6 mm. Plain bar b. 8 mm. Deformed bar. Total carried to summary 5. Walling 20x15x40 block work Pointing of all internal and external block wall surface in cement and sand Total carried to summary 6. Roofing Roof cover in G-32 corrugated galvanized iron sheet including flushing and roof ridges cover fixed to fix a sawn zigba purl in of at C/C 90 cm. Including asphalt washer (roof cover measured in horizontal projection.) Price includes eucalyptus truss with two coats of anti-termite Total carried to summary 7. Door Supply and fix single leaf metal in LTZ frame covered with 1mm. Thick corrugated sheet metal price includes monger, handle, cylderical normal lock, one coat of anti-rust and two coats of synthetic paint. a. Door size = 80cmx210cm Total carried to summary 8. Finishing Work 1M. wide semi-dressed stone pavement including 10 cm thick compacted red ash and joint pointed in cement sand mortar (1:3) price include excavation and cart away the excavated material from the site Supply and install 8 mt. PVC vent pipe complete with all accessories including vent cap. Total carried to summary | M2 M3 M3 M3 M3 M3 M2 M2 Kg. Kg. Kg. Kg. M3 M3 M2 M2 Kg. Kg. M2 M2 M2 Pcs. M2 Mt. | 23.75 27 17 10 26 1.20 4.29 5 39 25 75 100 0.40 0.48 7 6 13.80 63.64 26 52 13 4 14 4 | 8.00 38.00 17.00 13.00 170.00 380.00 250.00 110.00 10.50 11.00 18.00 22.00 365.00 365.00 120.00 115.00 10.50 11.00 100.00 35.00 170.00 700.00 200.00 180.00 | 190.00 1,026.00 289.00 130.00 1,635.00 4,420.00 4,420.00 456.00 1,072.50 550.00 490.50 275.00 1,350.00 2,200.00 6,394.00 146.00 175.20 840.00 690.00 144.90 700.04 2,696.14 2,600.00 1,820 .00 4,420.00 2,210.00 2,210.00 2,800.00 2,800.00 2,800.00 720.00 3,520.00 |